## Slide 1: IEEE 802.11ay Next Generation 60 GHz Communication for 100 Gb/s WiFi

## Slide 2
BLG433E
Computer
Communications
2018-2019 Fall Term
Prof. Dr. Sema Oktuğ
Muhammed Burak Buğrul
bugrul@itu.edu.tr
Kadir Emre Oto
otok@itu.edu.tr
Mustafa Efekan Pekel
pekelm@itu.edu.tr
Korel Chairoula
chairoulak@itu.edu.tr

## Slide 3: ABSTRACT
IEEE 802.11ay Task Group has defined new PHY and MAC specifications that enable 100 Gb/s communications due to enabling multi-Gb/s wireless local communications and reliability requirements of new applications such as AR/VR.
In this paper presentation, we are describing main design elements of IEEE 802.11ay.

## Slide 4: INTRODUCTION
While wireless technologies evolving, new applications and usage growth demand greater throughput and reliability with lower latencies.
IEEE 802.11ay Task Group was formed in 2015 in order to define PHY and MAC amendments that enable Wi-Fi devices to achieve 100 Gb/s using 60 GHz band.
DMG (Directional Multi-Gigabit) and EDMG (Enhanced Directional Multi-Gigabit) stations refer to devices that can support features of 802.11 and 802.11ay standards, respectively.

## Slide 5: Channel Bounding and Aggregation
IEEE 802.11ad only allows for single (2.16 GHz) channel transmission. 802.11ay includes mechanisms for channel bounding and aggregation.
In channel bounding, a single waveform covers at least two 2.16 GHz channels, whereas channel aggregation has a separate waveform for each channel.
IEEE 802.11ay mandates that EDMG STAs must support operation in 2.16 GHz channels. Channel aggregation of two channels and bonding of there or four 2.16 GHz channels optional.

## Slide 6: Directional MIMO Communication
To achieve both beamforming and multiplexing gain, 802.11ay defines new mechanisms to enable MIMO operation including Single-User MIMO (SU-MIMO) and Multi-User MIMO (MU-MIMO).
802.11ay also supports stations with dual-polarized antenna arrays. It allows for diversity gains and multiplexing in line-of-sight environments.
MIMO link supports is determined by different factors including the environment, the directivity of the antenna used and on whether antenna polarization is exploited.

## Slide 7: IEEE 802.11AY PHYSICAL LAYER

## Slide 8: EDMG Packet Format
A single packet format is defined for the three EDMG PHY modes: SC (single carrier), OFDM (orthogonal frequency division multiplexing) and control.
Not all fields are transmitted in EDMG packet. Some are used for single channel or channel bonding, SISO or MIMO transmission or beamforming training/ tracking.

## Slide 9: Non-EDMG Portion
Non-EDMG portion allows backward compatibility.
L-STF & L-CEF for packet detection, carrier frequency earning and timing
L-Header field is the same as the header field of 802.11ad packet, however some of its bits redefined.

## Slide 10: EDMG Portion
Only recognized by EDMG STAs
EDMG-Header-A field carries information to interpret EDMG packets (bandwidth, modulation, coding scheme, spatial streaming).
EDMG-STF and EDMG-CEF enable stations to estimate various signal parameters and the channel when channel bounding or MIMO utilized.
EDMG-Header-B is only included in MU-MIMO packets.

## Slide 11: Data Field Format
The data field consists of the payload data and possible padding (0s).
SC block size consists of 512 x NCB symbols, NCB is the number of utilized 2.16 GHz channels.
The control mode allow low SNR operation prior to beamforming (MCS 0).
Other MCS are based on BPSK, QPSK, 16 and 64 QAM modulations and LDPC codes with different rates
The achievable data rate for each MCS index depends on the number of spatial streams.

## Slide 12: Training Field Format
TRN field allows to transmit and receive beamforming training.
BRP (Beam Refinement Protocol) is a process to be able to improve its antenna configuration for transmission and reception.
TRN field redesigned in 802.11ay to increase efficiency and make it configurable.

## Slide 13: Training Field Format
In a BRP procedure, all TRN subfields are transmitted with the same antenna weight vector (AWV) as the data field.
AWV is vector of weights describing the excitation for each element of an antenna array.
This configuration allows receiver to switch AWVs when receiving different TRN subfields and determine an improved antenna configuration setting.

## Slide 14: Training Field Format
In a BRP procedure, transmitter uses different AWVs in the transmission of the TRN field while the receiver uses same AWV.
Three parameters define the format of a TRN-Unit used for transmit beamforming training.
EDMG TRN-Unit P, EDMG TRN-Unit M, EDMG TRN-Unit N

## Slide 15: Training Field Format
P transmits the TRN subfields at the same AWV in which the receiver uses this info to synchronize and estimate the channel
M enhances the robustness of the beamforming training process (may be transmitted with the same AWV over and over again)
N is the number of sequential TRN subfields with the same AWV

## Slide 16: IEEE 802.11AY MEDIUM ACCESS CONTROL LAYER

## Slide 17: Beacon Interval
Two main access periods:
  beacon header interval (BHI)
  data transmission interval (DTI)

## Slide 18: Beacon Header Interval
Beacon transmission interval (BTI)
Association beamforming training (ABFT)
Announcement transmission interval (ATI)

## Slide 19: Multiple Channel Access
To facilitate the coexistence of EDMG STAs with DMG STAs, the channel width of the primary channel is 2.16 GHz.
To enable the coexistence of DMG and EDMG STAs, network announcement and management frames need to be transmitted through primary channel.

## Slide 20: Multiple Channel Access Through Scheduling

## Slide 21: MIMO Channel Access
To perform a MIMO transmission, transmitter must obtain TXOP.
To this end, EDMG STAs that support MIMO maintain physical and virtual carrier sensing and perform the backoff procedure.

## Slide 22: IEEE 802.11AY BEAMFORMING CONTROL

## Slide 23: BF Training
Beamforming training is used to determine the appropriate transmit and receive antenna configurations for a pair of stations through two sub-phases.
IEEE 802.11ay includes several new beamforming training protocols, including SU-MIMO/MU-MIMO beamforming training, BRP transmit sector sweep and beamforming for asymmetric links.

## Slide 24: SU-MIMO Beamforming
SU-MIMO BF protocol consists of two consecutive phases: SISO phase and MIMO phase.
SISO Phase: In this phase, both STAs collect the necessary feedback for possible candidate sectors.

## Slide 25: SU-MIMO Beamforming
MIMO Phase enables the simultaneous training of transmit and receive sectors for each DMG antenna.
Four mandatory sub-phases:
SU-MIMO BF Setup, SU-MIMO BF training (SMBT), responder SMBT, SU-MIMO BF feedback

## Slide 26: MU-MIMO Beamforming
MU-MIMO BF enables an initiator and a group of responders to determine appropriate antenna configurations for simultaneous transmission of multiple data streams with minimum inter-stream interference.
802.11ay only supports downlink MU-MIMO transmission.

## Slide 27
MU-MIMO Beamforming
SISO Phase

## Slide 28
MU-MIMO Beamforming
MIMO Phase

## Slide 29: CONCLUSION
Design and experimental analysis of MIMO policies under different LoS and non-LoS conditions, different antenna directivities and with single-polarized or dual-polarized transmissions.
Design and implementation of adaptive dual-polarized arrays .
Design of low-power and low-complexity MIMO architectures for milimeter-wave that allow for flexible analog and digital beamforming and digital beamforming and advanced signal processing techniques.
IEEE 802.11ay advances provide opportunities for new research topics:

## Slide 30: THANKS!