## Slide 1
MOSFET

## Slide 2
MOSFET stands for metal-oxide semiconductor field-effect transistor.
Unlike BJT which is ‘current controlled’, the MOSFET is a voltage controlled device.
The MOSFET has “gate“, “Drain”, “Source” and “Body” terminals.
MOSFET
G-Gate
D-Drain
S-Source
B-Substrate or Body

## Slide 3: Types of MOSFETS
n-channel Enhancement Mode (nMOSFET) | p-channel Enhancement Mode (pMOSFET)
n-channel Depletion Mode (nMOSFET) | p-channel Depletion Mode (pMOSFET)

## Slide 4: Cross-Sectional View of n channel Enhancement Mode Transistor
Enhancement mode
Also known as Normally Off transistors.
▫ A voltage must be applied to the gate of the transistor, at least equal to the threshold voltage, to create a conduction path between the source and the drain of the transistor before current can flow between the source and drain.
Cross-Sectional View of p channel Enhancement Mode Transistor

## Slide 5: p channel Depletion Mode Transistor
n channel Depletion Mode Transistor
Depletion mode
Also known as Normally On transistors.
A voltage must be applied to the gate of the transistor, at least equal to the threshold voltage, to destroy a conduction path between the source and the drain of the transistor to prevent current from flowing between the source and drain.

## Slide 6: Operation of a Enhancement mode transistor
Substrate
Channel
Drain
Insulator
Gate
VGS > 0
n type operation
Positive gate bias attracts electrons into channel.
Channel now becomes more conductive
More
electrons
Source
VSD
VGS
A voltage must be applied to the gate of the transistor, at least equal to the threshold voltage, to create a conduction path between the source and the drain

## Slide 7: Before electron inversion layer is formed
After electron inversion layer is formed
(Enhancement mode)
With no bias voltage applied to the gate terminal, there exists two back-to-back pn junctions between the drain and the source. No current flows from drain to source (the resistance will be on the order of 1012 Ω).

## Slide 8: Symbols for n channel Enhancement Mode MOSFET
Symbols for p channel Enhancement Mode MOSFET
VGS ≥ 0V, VDS ≥ 0V
VTN is positive
VGS ≤ 0V, VDS ≤ 0V
VTP is negative

## Slide 9: Symbols for n channel Depletion Mode MOSFET
Symbols for p channel Depletion Mode MOSFET

## Slide 10: Working Modes
ID
VDS
0.1 v
increasing
VGS
triode
saturation
VDS>VGS-VT
VDS<VGS-VT
(Enhancement mode)

## Slide 11: Triode Region A voltage-controlled resistor @small VDS
G
p
n+
n+
metal
S
D
B
oxide
+
-
+++
+++
- - - -
VGS1>Vt
p
n+
n+
metal
S
D
B
oxide
+
-
+++
+++
+++
- - - - - -
VGS2>VGS1
p
n+
n+
metal
S
D
B
oxide
+
-
+++
+++
+++
- - - - - - - - -
VGS3>VGS2
+++
ID
VDS
0.1 v
increasing
VGS
Increasing VGS puts more charge in the channel, allowing more drain current to flow
cut-off
Positive gate bias attracts electrons into channel.
(Enhancement mode)

## Slide 12: Saturation Region occurs at large VDS
p
n+
n+
metal
source
S
gate
G
drain
D
body
B
oxide
+
-
+++
+++
+++
VDS large
As the drain voltage increases, the difference in voltage between the drain and the gate becomes smaller. At some point, the difference is too small to maintain the channel near the drain  pinch-off
(Enhancement mode)

## Slide 13
Saturation Region occurs at large VDS
p
n+
n+
metal
source
S
gate
G
drain
D
body
B
oxide
+
-
+++
+++
+++
VDS large
The saturation region is when the MOSFET experiences pinch-off. Pinch-off occurs when VG - VD is less than VT.
(Enhancement mode)

## Slide 14
Saturation Region occurs at large VDS
p
n+
n+
metal
source
S
gate
G
drain
D
body
B
oxide
+
-
+++
+++
+++
VD>>Vs
VGS - VDS < VT or VGD <
or VDS > VGS - VT
VT
(Enhancement mode)

## Slide 15: Saturation Region once pinch-off occurs, there is no further increase in drain current
(Enhancement mode)

## Slide 16
n-channel MOSFET Basic Operation
Operation in the Cutoff region
pn junction: reverse bias
iD=0
for vGS<Vt0
When vGS=0 then iD=0 until vGS>Vt0 (Vt0 –threshold voltage)
(Enhancement mode)

## Slide 17
n-channel MOSFET Basic Operation
Operation in the Triode Region
(K is defined by the electrical and physical parameters of the MOSFET)

## Slide 18
n-channel MOSFET Basic Operation
Operation in the Saturation Region (vDS is increased)
Tapering
of the
channel
- increments
of iD are
smaller
when
vDS is
larger

## Slide 19
p-channel MOSFET Basic Operation
It is constructed by interchanging the n and p regions of n-channel MOSFET.
Characteristic
Symbol

## Slide 20
Load-Line Analysis of NMOS Amplifier
It is a graphical analysis similar to load-line analysis of pn diode.
Circuit Analysis:
Input
loop
Output loop
Load line
vGS
vDS
We look for the operating point

## Slide 21
Load-Line Analysis of NMOS Amplifier
Exercise:
Draw the Load line
RD= 1 kW

## Slide 22
Load-Line Analysis of NMOS Amplifier
Load line
Taking iD=0 or vDS=0 we find out the load line and the operating point Q for VGS=4V
Points A & B intersection of curve and the load-line for the maximum and the minimum gate voltage

## Slide 23
Input signal
Load-Line Analysis of NMOS Amplifier
(peak-to-peak amplitude is 2V)
12V peak-to-peak
Inverse operation
The positive peak of the input occurs at the same time as the min. value of vDS. The output is not a symmetrical sinusoid! (nonlinear distortion)
vDS(t)
vin(t)
2V peak-to-peak

## Slide 24
Self Bias Circuits
Analysis of amplifier circuits is often undertaken in two steps:
(1) The DC circuit analysis to determine the Q point. It involves the
nonlinear equation solution or the load-line method. This is called bias
analysis
The fixed-plus self-bias circuit
Exercise:
Find VG voltage as a function of VDD, R1 and R2
Input
Output
+
vG
_

## Slide 25
Self Bias Circuits
Analysis of amplifier circuits is often undertaken in two steps:
(1) The DC circuit analysis to determine the Q point. It involves the
nonlinear equation solution or the load-line method. This is called bias
analysis
The fixed-plus self-bias circuit
Input
Output
+
vG
_

## Slide 26
Self Bias Circuits
Analysis of amplifier circuits is often undertaken in two steps:
(1) The DC circuit analysis to determine the Q point. It involves the
nonlinear equation or the load-line method. This is called bias
analysis
(2) Use a linear small-signal equivalent circuit to determine circuit
parameters
Equivalent circuit
Analysis…
vGS
vDS
find vGS
For saturation region

## Slide 27
Self Bias Circuits
Plot of
and
Disregarded root for vGS<Vt0
Use only larger root for vGS and smaller for iD
For saturation region

## Slide 28
Self Bias Circuits
Analysis of amplifier circuits is often undertaken in two steps:
(1) The dc circuit analysis to determine the Q point. It involves the
nonlinear equation or the load-line method. This is called bias
analysis
(2) Use a linear small-signal equivalent circuit to determine circuit
parameters
Equivalent circuit
Analysis…
vGS
vDS
For saturation region
find iD

## Slide 29
Self Bias Circuits
Analyze the self-bias circuit shown. The transistor has K=1mA/V2, Vto=2V.
find vGS
find iD
find vDS
(For saturation region)

## Slide 30
Small-Signal Equivalent Circuit for FETs
Output signal from an amplifier using MOSFET can be effectively modulated by small changes of input signal current. In this way it is possible to make small changes from the Q point.
Symbols:
The total quantities: iD(t), vGS(t)
The DC point values: IDQ, VGSQ
The signal id(t), vgs(t)
Characteristic

## Slide 31
Small-Signal Equivalent Circuit -Transconductance
Schematic
We define the transconductance as

## Slide 32
More Complex Equivalent Circuits
For more accurate analyses of FET transistor we have to add more components to an equivalent circuit.
Drain resistor: account for the effect of vDS on the drain current
Correction for id

## Slide 33
Drain Resistance Calculation
so at vGS=4V

## Slide 34
Common-Source Amplifier
Schematic
G
D
S
The dc supply voltage acts as a short circuit for the ac current.
Equivalent circuit

## Slide 35
Common-Source Amplifier
Schematic
ac signal
Cs -bypass C
C1, C2 -coupling C
G
D
S
The dc supply voltage acts as a short circuit for the ac current.
Equivalent circuit

## Slide 36
Common-Source Amplifier: Gain, Rin and Rout
Equivalent circuit (once more)
Voltage gain
Input resistance
From bias point analysis