## Slide 1: BJT Transistors

## Slide 3
The transistor was probably the most important invention of the 20th Century, and the story behind the invention is one of clashing egos and top secret research.
First - BJTs
Reference:
Bell Labs Museum
B. G. Streetman & S. Banerjee ‘Solid State Electronic Devices’, Prentice Hall 1999.

## Slide 4
Picture shows the workbench of John Bardeen (Stocker Professor at OU) and Walter Brattain at Bell Laboratories. They were supposed to be doing fundamental research about crystal surfaces.
The experimental results hadn't been very good, though, and there's a rumor that their boss, William Shockley, came near to canceling the project. But in 1947, working alone, they switched to using tremendously pure materials.
It dawned on them that they could build the circuit in the picture. It was a working amplifier! John and Walter submitted a patent for the first working point contact transistor.
Interesting story…

## Slide 5
Shockley was furious and took their work and invented the junction transistor and submitted a patent for it 9 days later.
The three shared a Nobel Prize in 1955. Bardeen and Brattain continued in research (and Bardeen later won another Nobel).
Shockley quit to start a semiconductor company in Palo Alto. It folded, but its staff went on to invent the integrated circuit (the "chip") and to found Intel Corporation.
By 1960, all important computers used transistors for logic, and ferrite cores for memory.
Interesting story…

## Slide 6
Point-Contact Transistor –
first transistor ever made

## Slide 7: Recall p-n junction
P
N
W
Vappl > 0
-
+
N
P
W
Vappl < 0
-
+
Forward bias, + on P, - on N
(Shrink, Vbi)
Allow holes to jump over barrier
into N region.
Reverse bias, + on N, - on P
(Expand, Vbi)
Remove holes and electrons away
from depletion region
I
V
I
V

## Slide 8: So if we combine these by fusing their terminals…
P
N
W
Vappl > 0
-
+
N
P
W
Vappl < 0
-
+
Holes from P region (“Emitter”) of 1st PN junction are
driven by Forward Bias of 1st PN junction into central N region (“Base”)
Driven by Reverse Bias of 2nd PN junction from Base into P region of
2nd junction (“Collector”)

## Slide 9
Basic models of BJT
Diode
Diode
Diode
Diode
npn transistor
pnp transistor

## Slide 10
Basic models of BJT
Emitter layer is heavily doped

## Slide 11: npn BJTs
It contains three semiconductor layers: one p-layer and two n-layers.
The area of collector layer is largest. So it can dissipate heat quickly.
Area of base layer is smallest and it is very thin layer.
Area of emitter layer is medium.
Collector layer is moderately doped. So it has medium number of charges (electrons).
Base layer is lightly doped. So it has a very few number of charges (holes).
Emitter layer is heavily doped. So it has largest number of charges (electrons).
THE P-LAYER IS SANDWICHED BETWEEN TWO N-LAYERS.
The junction between collector layer and base layer is called as collector-base junction or c-b junction.
The junction between base layer and emitter layer is called as base-emitter junction or b-e junction.
The two junctions have almost same potential barrier voltage of 0.6V to 0.7V, just like in a general purpose rectifier diode.

## Slide 12: npn BJTs
The collector is connected to high positive voltage with respect to base i.e. Vcb is very high. So c-b junction is reverse biased.
Vbe is low.When we increase Vbe ≥ 0.7V (the value 0.7V is a typical value of potential barrier voltage) the transistor is forward biased.
Now large number of electrons in emitter layer is repelled by negative terminal of Vbe and they flow towards b-e junction.
They cross the junction and enter into small base layer. Here some electrons combine with holes. Also some of them are attracted by positive terminal of Vbe and remaining maximum number of electrons flow into collector layer, crossing the second junction i.e. c-b junction.
The resident electrons of collector are repelled by these (guest) electrons and thus, then all the electrons are present in collector layer are attracted by positive terminal of Vcb. Thus, all these electrons complete their journey back into emitter layer and produce conventional currents in the transistor as shown in the above circuit.

## Slide 13: npn BJTs
Now when Vbe is still increased, more electrons are repelled by negative terminal of Vbe. So base-emitter junction is more and more forward biased. Thus the base current (Ib) increases, which in turn increases Ic.
Collector current (Ic) is controled by base current (Ib)
Hence, we can say that collector current (Ic) is the function of base current (Ib).
In all this process, maximum number of electrons from emitter layer flow into collector layer. So collector current is ALMOST EQUAL to emitter current. Hence we say that, collector current is proportional to emitter current.

## Slide 14
When there is no IB current almost no IC flows
When IB current flows, IC can flow
The device is a current controlled current device
Operational modes
can be defined
based on
VBE and VBC
BJTs – Operation Modes
(BJT will operates in one of following three region)

## Slide 15: Bipolar Junction Transistors: Operation Modes
Bias Mode | E-B Junction | C-B Junction
Saturation | Forward | Forward
Active | Forward | Reverse
Cutoff | Reverse | Reverse
Saturation : In this method both the junctions are forward biased. This method is not useful as the transistor is in “saturation” and the current cannot be controlled easily.
Cutoff: In this method both the junctions are reverse biased. This method is also not useful as the transistor is in “cut-off” state since current is zero.
Active: This is the most common and popular method used in transistor biasing. In this method, the base-emitter junction is forward biased and collector-base junction is reverse biased. So by adjusting base voltage we can control total current in the transistor easily.

## Slide 16
BJT Operating Regions and I V Curves
Input characteristics
  the input takes the form of a forward-biased pn junction
  the input characteristics are similar to a semiconductor diode
Output characteristics
  region near to the origin is the saturation region
  this is normally avoided in linear circuits

## Slide 17
Operation mode: vBE is forward & vBC is reverse (Active mode)
The Shockley equation
IES=saturation current (10-12-10-16A); VT=kT/q -thermal V (26mV)
The Kirchhoff’s laws
It is true regardless of the bias
conditions of the junction
Useful
parameter
BJTs – Current & Voltage Relationships

## Slide 18
Relationship between the collector current and the base current
  characteristic is approximately linear
  magnitude of collector current is generally many times that of the base current
  the device provides current gain
It is true regardless of the bias
conditions of the junction
Useful
parameter

## Slide 19
Please calculate the current gain () of this transistor
Example:

## Slide 20
Voltage polarities and current flow in transistors biased in the active mode.
Notes: sedr42021_0514a.jpg

## Slide 21
BJTs – Characteristics
Input
Output
VBC<0 or equivalently VCE>VBE
If VCE<VBE the B-C junction is also forward bias and IC decreases (saturation region)
Remember VBE has to be greater
than 0.6-0.7 V

## Slide 22
BJTs – Load line analysis
Input loop
if iB=0
if vBE=0
vBB
VBB/RB

## Slide 23
BJTs – Load line analysis
Output loop

## Slide 24
or
Assumption:
It is assumed that |VBE| = 0.7V in the active and saturation regions.
Load Line Analysis:
Can be performed in order to determine |VBE| value of transistor in the active and saturation regions.

## Slide 25
Problem : Analyze the circuits shown in Figure (a) to determine I and V. For all transistors, assume that β = 100 and |VBE| = 0.7V in the active region. (RC=5kΩ, RE=7.07kΩ)
Notes: sedr42021_0515a.jpg

## Slide 26
Problem : Analyze the circuits shown in Figure (a) to determine I and V. For all transistors, assume that β = 100 and |VBE| = 0.7V in the active region.
Notes: sedr42021_0515a.jpg

## Slide 27: DC Biasing Circuits of BJTs

## Slide 28: Objectives
State the purpose of DC biasing circuits.
Plot the DC load line given the value of VCC and the total collector-emitter circuit resistance.
Describe the Q-point of an amplifier.
Describe and analyze the operations of various bias circuits:
  base-bias circuits
  voltage-divider bias circuits
  emitter-bias circuits
  collector-feedback bias circuits
  emitter-feedback bias circuits

## Slide 29: A generic DC load line.

## Slide 30: Example
Plot the DC load line for the circuit shown in Fig.

## Slide 31: Example
Plot the DC load line for the circuit shown in Fig. Then, find the values of VCE for IC = 1, 2, 5 mA respectively.
IC (mA) | VCE (V)
1 | 9
2 | 8
5 | 5

## Slide 32: Optimum Q-point with amplifier operation.

## Slide 33: Q-point is not at optimum location
Clipping
Clipping
Amplitude of input signal can not be too great

## Slide 34: BIAS CIRCUITS
b = DC current gain = hFE
1. Base bias (fixed bias).

## Slide 35: Example
Construct the DC load line for the circuit and plot the Q-point. Determine whether the circuit is midpoint biased.

## Slide 36: Example
The circuit is midpoint biased.

## Slide 37: (Q-point shift)
The transistor has values of hFE = 100 when T = 25 °C and hFE = 150 when T = 100 °C. Determine the Q-point values of IC and VCE at both of these temperatures. VBE=0.7V
Temp(°C) | IB (mA) | IC (mA) | VCE (V)
25 | 20.28 | 2.028 | 3.94
100 | 20.28 | 3.04 | 1.92
(250C)
Q(1000C)

## Slide 38: Base bias characteristics.
Advantage: Circuit simplicity.
Disadvantage: Q-point shift with temp.
Applications: Switching circuits only.
Circuit recognition: A single resistor (RB) between the base terminal and VCC. No emitter resistor.

## Slide 39: Base bias characteristics.
Load line equations:
Q-point equations:

## Slide 40: 2. Voltage divider bias.
Assume that I2 > 10IB.
Assume that ICQ @ IE (or hFE >> 1). Then

## Slide 41: Example
Determine the values of ICQ and VCEQ for the circuit shown in Fig.
Because ICQ @ IE (or hFE >> 1),

## Slide 42: Example
Verify that I2 > 10 IB

## Slide 43: Which value of hFE do I use?
Transistor specification sheet may list any combination of the following hFE max. hFE min or hFE typ. Use typical value if there is one. Otherwise, use

## Slide 44: Example
A voltage-divider bias circuit has the following values:
R1 = 1.5 kW, R2 = 680 W, RC = 260 W, RE = 240 W and VCC = 10 V. Assuming the transistor is a 2N3904, determine the value of IB for the circuit.

## Slide 45: Stability of Voltage Divider Bias Circuit
The Q-point of voltage divider bias circuit is less dependent on hFE than that of the base bias (fixed bias).
For example, if IE is exactly 10 mA, the range of hFE is 100 to 300. Then
ICQ hardly changes over the entire range of hFE.

## Slide 46: Load line for voltage divider bias circuit.
Circuit values are from previous example.

## Slide 47: Voltage-divider bias characteristics.
Circuit recognition: The voltage divider in the base circuit.
Advantages: The circuit Q-point values are stable against changes in hFE.
Disadvantages: Requires more components than most other biasing circuits.
Applications: Used primarily to bias linear amplifier.

## Slide 48: Voltage-divider bias characteristics.
Load line equations:
Q-point equations (assume that hFERE > 10R2):

## Slide 49: 3. Emitter bias.
Assume that the transistor operation is in active region.
Assume that hFE >> 1.

## Slide 50: Example
Determine the values of ICQ and VCEQ for the amplifier shown in Fig.

## Slide 51: Load Line for Emitter-Bias Circuit

## Slide 52: Emitter-bias characteristics.
Circuit recognition: A split (dual-polairty) power supply and the base resistor is connected to ground.
Advantage: The circuit Q-point values are stable against changes in hFE.
Disadvantage: Requires the use of dual-polarity power supply.
Applications: Used primarily to bias linear amplifiers.

## Slide 53: Emitter-bias characteristics.
Load line equations:
Q-point equations:

## Slide 54: 4. Collector-feedback bias.

## Slide 55: Example
Determine the values of ICQ and VCEQ for the amplifier shown in Fig.

## Slide 56: Circuit Stability of Collector-Feedback Bias
hFE increases
IC increases (if IB is the same)
VCE decreases
IB decreases
IC does not increase that much.
Good Stability. Less dependent on hFE and temperature.

## Slide 57: Collector-Feedback Characteristics
Circuit recognition: The base resistor is connected between the base and the collector terminals of the transistor.
Advantage: A simple circuit with relatively stable Q-point.
Disadvantage: Relatively poor AC characteristics.
Applications: Used primarily to bias linear amplifiers.

## Slide 58: Collector-Feedback Characteristics
Q-point relationships:

## Slide 59: 5. Emitter-feedback bias.

## Slide 60: Example

## Slide 61: Circuit Stability of Emitter-Feedback Bias
hFE increases
IC increases (if IB is the same)
VE increases
IB decreases
IC does not increase that much.
IC is less dependent on hFE and temperature.

## Slide 62: Emitter-Feedback Characteristics
Circuit recognition: Similar to voltage divider bias with R2 missing (or base bias with RE added).
Advantage: A simple circuit with relatively stable Q-point.
Disadvantage: Requires more components than collector-feedback bias.
Applications: Used primarily to bias linear amplifiers.

## Slide 63: Emitter-Feedback Characteristics
Q-point relationships:

## Slide 64
BJTs – Testing

## Slide 65
npn
BJTs – Practical Aspects

## Slide 67
npn

## Slide 68
npn

## Slide 69: Problem : Analyze the circuits shown in Figure to determine I and V. For all transistors, assume that β = 100 and |VBE| = 0.7V in both the active and saturation regions.

## Slide 70
Problem : Analyze the circuits shown in Figure to determine I and V. For all transistors, assume that β = 100 and |VBE| = 0.7V in both the active and saturation regions.

## Slide 71: Problem: Suppose that npn transistor has VBE = 0.7V. Determine IC and VCE for transistor and output voltage.
Base current is small, so
Emitter voltage
VE = VB – VBE = 2.7 – 0.7 = 2.0 V
Emitter current
Since IB is small, collector current IC  IE = 2 mA
Output voltage = VCC – ICRC = 10 - 2 mA 2.2 k = 5.6 V

## Slide 72: Problem: The transistors shown in figure operate in active region and have β = 100, VBE=0.7V. Determine IC and VCE for each transistor.
I1
IE2
VBE

## Slide 73: Problem: Analyze the circuit of Figure determine IC and VCE. (β = 100, VBE=0.7V)
I
I1
IE
IB
IC

## Slide 74: Problem: Consider the emitter-follower amplifier of Figure. Draw the DC circuit and find ICQ (β = 100, VBE=0.7V).
I1

## Slide 75
Consider the amplifier shown above. Use the following parameters for your calculations. Transistor parameters : β=150, VBE=0.6V
a. Performing DC analysis and calculate DC operating values of the transistor.

## Slide 76
Early Effect
İdeal: Slope is zero
Reallity: Slope is not zero. This nonlinear behaviour is modeled by ‘Early Voltage’ (VA).

## Slide 77
Circuit whose operation is to be analyzed graphically.
Graphical construction for the determination of the dc base current in the circuit (output)
Graphical construction for the determination of the dc base current in the circuit (input)
Small-Signal Analysis
A small signal component vi is superimposed on the DC voltage
Notes: sedr42021_0527.jpg

## Slide 78
Graphical determination of the signal components vbe, ib, ic, and vce when a signal component vi is superimposed on the dc voltage VBB
Small-Signal Analysis
Notes: sedr42021_0530a.jpg

## Slide 79
Small-Signal Equivalent Circuit
Small signal equivalent circuit for BJT:
and
Transistor is modeled by using input resistance and output current
Assumption: Early Voltage (VA) is infinite.

## Slide 80
DC ANALYSIS
Replace all capacitors with OPEN circuits.
Set all AC sources to zero, because they have zero signal component!!!
RS
R1
RC
R2
Cin
Cout
+
vs
-
+
RL vo
-
Q1
vin
+
-
CE
VCC
RE

## Slide 81
Constructing the Small-Signal Equivalent Circuit
To construct small-signal equivalent circuit for entire amplifier, we:
Replace the BJT by its small-signal model.
Replace all capacitors with short circuits.
Set all DC sources to zero, because they have zero signal component!!!
The result is the small-signal equivalent circuit of the amplifier:
RS
R1
RC
R2
Cin
Cout
+
vs
-
+
RL vo
-
Q1
vin
+
-
CE
VCC

## Slide 82
First perform DC analysis to find small-signal equivalent parameters at the operating point.
Then:
To construct small-signal equivalent circuit for entire amplifier, we:
Replace the BJT by its small-signal model.
Replace all capacitors with short circuits.
Set all DC sources to zero, because they have zero signal component!!!
The result is the small-signal equivalent circuit of the amplifier:
Small-Signal Analysis

## Slide 83
Find voltage gain:
Find input impedance:
Small-Signal Analysis
Avoc: Open circut gain. Gain without ‘Load’

## Slide 84
Find power gain:
Find current gain
Small-Signal Analysis
Find output impedance:

## Slide 85
The parameters of the transistor are β = 100, VBE=0.7V and VA =∞.
(a) Find the dc voltages at the base and emitter terminals.
(b) Find RC such that VCEQ = 3.5 V.
(c) Assuming CC and CE act as short circuits, determine the small-signal voltage gain Av = vo /vs.

## Slide 86
Consider the amplifier shown above. Use the following parameters for your calculations. Transistor parameters : β=200, VBE=0.7V, VT=25mV, VA= ∞
a. Find VB and VC of the transistor by performing DC analysis.
b. Find the small signal values of rin, rout, and vout/vin.

## Slide 87
Consider an amplifier shown below. Suppose that the value of the coupling capacitors Cc1 and Cc2 are high enough, so they can be considered shorted in small signal analysis. Find the small signal values of rin, rout, and vout/vin.
NPN Transistor Parameters: VBE = 0.7, β = 40, VA = ∞, VT = 25 mV.

## Slide 88
For the circuit shown on the left, transistor parameters for identical T1 and T2 are VA = ∞, VT = 25 mV, |VBE| = 0,6 V, and hfe = hFE = = β = 100.
a. Determine DC collector currents.
b. Find the small signal voltage gain vo/vin.
c. Determine the input and output resistances.

## Slide 89
Transistor as an amplifier:
Transistors are often used as amplifiers to increase input signal in radios, televisions and some other applications .The circuit may be designed to increase the current or voltage level.

## Slide 90
Amplifier Classes:
Class A Amplifiers
Class AB Amplifiers
Class B Amplifiers
Class C Amplifiers
They are defined by the length of their conduction state over some portion of the output waveform.

## Slide 91: BJT Class A Amplifiers
In a class A amplifier, the transistor conducts for the full cycle of the input signal (360°)
  used in low-power applications.
The transistor is operated in the active region, between saturation and cutoff.
  saturation is when both junctions are forward biased. the transistor is in cutoff when IB = 0.
The load line is drawn on the collector curves between saturation and cutoff.

## Slide 92: BJT Class A Amplifiers

## Slide 93: BJT Class B Amplifiers
When an amplifier is biased such that it operates in the linear region for 180° of the input cycle and is in cutoff for 180°, it is a class B amplifier.
  Class B amplifier is more efficient than a class A. The transistors in a class B amplifier must be biased above cutoff to eliminate crossover distortion.

## Slide 94: The BJT as a Switch
When used as an electronic switch, a transistor normally is operated alternately in cutoff and saturation
  A transistor is in cutoff when the base-emitter junction is not forward-biased. VCE is approximately equal to VCC
  When the base-emitter junction is forward-biased and there is enough base current to produce a maximum collector current, the transistor is saturated