## Slide 1: Introduction to Electronics EHB222E

## Slide 2
Grading
Grading Method
Two Midterm Exams: 40%
Homework 5%
Quiz 5%
Final Exam: 50%
Attendence %50

## Slide 3
Introduction
Semiconductors & Doping, Basics of pn junction
Diodes
BJT Transistors
MOSFET Transistors
Operational Amplifiers
Introduction to Electronics

## Slide 4: What is Electricity?
Electricity is generated from the motion of tiny charged atomic particles called electrons and protons!
Protons = +
Electrons = -

## Slide 5
What is Current?
When electrons flows through a conductor
Only some materials have free electrons inside.
Conductors:
YES!
Insulators:
NO!
No free electrons = No current
We call this flow as “current.”
silver
copper
gold
aluminium
iron
steel
brass
bronze
mercury
graphite
salty water
glass
rubber
oil
asphalt
fiberglass
porcelain
ceramic
quartz
(dry) cotton
(dry) paper
(dry) wood
plastic
air
diamond
pure water

## Slide 6: How Does Current Flow?
Current can only flow through conductors
+++
Metal wires (conductors)
Current flow

## Slide 7: When Does Current NOT Flow?
+++
Plastic material (insulators)
Current cannot flow through insulators
No current flow

## Slide 8: Note that Air is an Insulator
+++
Air
Current cannot flow through insulators
No current flow
That’s why a battery doesn’t discharge if left on its own.

## Slide 9: Current
Current is the amount of electric charge (coulombs) flowing past a specific point in a conductor over an interval of one second.
1 ampere = 1 coulomb/second
Electron flow is from a lower potential (voltage) to a higher potential (voltage).

## Slide 10
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
electron motion
positive current direction
Sign Convention for Current Flow
Electrons carry negative charge
Positive current flow is in opposite direction

## Slide 11: Current Flow
The direction of current flow is indicated by an arrow.
Note: The voltage sources in the circuit flow current through nodes and wires.
+
_
Voltage Source

## Slide 12: What is Voltage?
V = “Electrical pressure”
- measured in volts.
Voltage is the difference in energy level from one end of the battery (or any other energy source) to the other.
The energy difference causes the positive charges to move from a higher to to lover voltage in a closed circuit

## Slide 13: A battery in an electrical circuit plays the same role as a pump in a water system.
A battery establishes a difference of potential that can pump electrons.
A battery pushes the electrons through the conductor.

## Slide 14
Conducting wires
Electronic elements
Two or more nodes connected just by wires can be considered as one single node.
Electric Circuit
Group of nodes connected only by wires
One big node
One big node
A single node
Nodes are Connected
by Wires Only

## Slide 15
I1 = I2 + I3
Diagram b shows a mechanical analogy
From Conservation of Charge

## Slide 16: Kirchhoff’s Current Law
The sum of currents flowing into a node must be balanced by the sum of currents flowing out of the node.
i1
i2
i3
node
i1 flows into the node
i2 flows out of the node
i3 flows out of the node
i1 = i2 + i3
Gustav Kirchoff was an 18th century German mathematician

## Slide 17
This equation can also be written in the following form:
i1
i2
i3
node
Kirchhoff’s Current Law: i1 = i2 + i3
i1 – i2 – i3 = 0
A formal statement of Kirchhoff’s Current Law:
(i2 and i3 leave the node, hence currents –i2 and –i3 enter the node.)
The sum of all the currents entering a node is zero.

## Slide 18
2.5 mA
4 mA
i4
i2
i3
Example 1: Kirchhoff’s Current Law:
io
Q: How much is the current Io ?
A: io = 2.5 mA + 4 mA = 6.5 mA
Note that a “node” need not be a discrete point
The dotted circle is a node with 2.5 mA entering
Hence i2 = 2.5 mA exits the “node”.
Similarly, i3 = 4 mA.
From KCL, i4 = i2 + i3 = 6.5 mA, and Io = i4

## Slide 19
Example 2: Kirchhoff’s Current Law:
Q: How much are the currents i1 and i2 ?
A: i2 = 10 mA – 3 mA = 7 mA
i1 = 10 mA + 4 mA = 14 mA
+
_
i1
4 mA
i2
10 mA
3 mA
4 mA + 3 mA + 7 mA = 14 mA
node

## Slide 20
Sometimes Kirchhoff’s Current Law is abbreviated just by
KCL
The net current entering a node must be zero.
The sum of all currents entering a node must be zero.
Whatever flows into a node must come out.
Review: Different ways to state KCL:
more to follow…

## Slide 21
Voltage (Difference in energy level )
Voltages are measured across the nodes of a circuit.
The direction of a voltage is indicated by + and – signs.
Remember: The voltage sources in a circuit flow
current through the conductors.
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–

## Slide 22: Kirchhoff’s Voltage Law
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
The voltage measured between any two nodes does not depend of the path taken.
voltage
Example of KVL:
v1= v2 + v3
Similarly:
v1= v2 + v4
voltage
and:
v3= v4
voltage

## Slide 23
This equation can also be written in the following form:
Kirchhoff’s Voltage Law: v1 = v2 + v3
–v1 + v2 + v3 = 0
A formal statement of Kirchhoff’s Voltage Law:
The sum of voltages around a closed loop is zero.
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–

## Slide 24: Using the Formal Definition of KVL
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
Sum the voltages that are encountered around the loop.
Define an arrow direction around a closed loop.
If the arrow first encounters a plus sign, enter that voltage with a (+) into the KVL equation.
If the arrow first encounters a minus sign, enter that voltage with a (–) into the KVL equation.
For the inner loop :
–v1 + v2 + v3 = 0
“The sum of voltages around a closed loop is zero.”
–v4 – v2 + v1 = 0
For the outer loop:

## Slide 25
Q: How much is the voltage Vo ?
A: Vo = 3.1 V + 6.8 V
Vo
_
+
+ 3.1V –
+
6.8 V
–
Example 1: Kirchhoff’s Voltage Law:
A: v4 = 6.8 V
Q: How much is the voltage v4 ?
+
v4
_

## Slide 26
Example 2: Kirchhoff’s Voltage Law:
Q: If v1 = 10 V and v5 = 2 V, what are v2, v3, and v4?
A: -v1 + v2 = 0  v2 = 10 V
-v2 + v3 + v5 = 0  v3 = 10 V – 2 V = 8 V
-v4 + v5 = 0  v4 = 2 V
+
_
+
v1 = 10 V
–
+
v2
–
+
v4
–
+
v5= 2 V
–
+ v3 –

## Slide 27
Electronic Circuits
Circuits are obtained by connecting electronic elements
Typical electronic elements are
diodes
resistors,
capacitors,
inductors

## Slide 28: Ohm’s Law & Resistors
Assume that the wires are “perfect conductors”
The unknown circuit element limits the flow of current.
The resistive element has resistance R
Let us remind the Ohm’s Law
Georg Ohm
+
_
V
V
R = ——
I
V
I = ——
R

## Slide 29: Ohm’s Law
Voltage drop across a resistor is proportional to the current flowing through the resistor
If the resistor is a perfect conductor (or a short circuit)
R = 0 ohm, then
v = iR = 0 V
no matter how much current is flowing through the resistor

## Slide 30: Resistors in Series

## Slide 31: Resistors in Parallel

## Slide 32: Resistors in Parallel

## Slide 33: Voltage Divider

## Slide 34: Equivalent Resistance – Complex Circuit

## Slide 35: Maximum Charge on a Conductor
Earth
Battery
Conductor
-
-
-
-
-
-
-
-
-
-
-
-
-
-
e-
e-
A battery establishes a difference of potential that can pump electrons e- from a ground (earth) to a conductor
There is a limit to the amount of charge that a conductor can hold without leaking to the air. There is a certain capacity for holding charge.

## Slide 36: Capacitance
The capacitance C of a conductor is defined as the ratio of the charge Q on the conductor to the potential V produced.
Capacitance:
Earth
Battery
Conductor
-
-
-
-
-
-
-
-
-
-
-
-
-
-
e-
e-
Q, V

## Slide 37
The Capacitor
Capacitors are one of the fundamental passive components. In its most basic form, it is composed of two plates separated by a dielectric.
The ability to store charge is the definition of capacitance.
Dielectric
Conductors

## Slide 38
The Capacitor
Initially uncharged
Charging
Fully charged
Source removed
The charging process…
A capacitor with stored charge can act as a temporary battery.

## Slide 39
Capacitors in Parallel:

## Slide 40
Capacitors in Series:

## Slide 41: Electromagnetism
A wire carrying a current I produces a magnetic field

## Slide 42
Inductance
Energy Storage Devices
Stores energy in an magnetic field created by the electric current flowing through it.
The flow of current through an inductor creates a magnetic field
If the current flowing through the inductor drops, the magnetic field will also decrease and energy is released through the generation of a current.
B field

## Slide 43: Inductors
Generally - coil of conducting wire
  Usually wrapped around a solid core. If no core is used, then the inductor is said to have an ‘air core’.

## Slide 44: Voltage and Current Relation
Consider the circuit shown here
  inductor is initially un-energised
    current through it will be zero
  switch is closed at t = 0
  I is initially zero
    hence VR is initially 0
    hence VL is initially V
  as the inductor is energised:
    I increases
    VR increases
    hence VL decreases
    we have exponential behaviour

## Slide 45
Both the voltage and current have an exponential forms
L , inductance, has the units of Henries (H)
1 H = 1 V.sn/A
C , capacitance, has the units of Farad (F)
1 F = 1 A.sn/V

## Slide 46: Inductors in Series

## Slide 47: Inductors in Parallel

## Slide 48: Example 1
Determine I, the current flowing out of the voltage source.
  Use KCL
    1.9 mA + 0.5 mA + I are
    entering the node.
    3 mA is leaving the node.
    V1 is generating power.

## Slide 49: Example 2
Suppose the current through R2 was entering the node and the current through R3 was leaving the node.
  Use KCL
    3 mA + 0.5 mA + I are
    entering the node.
    1.9 mA is leaving the node.
    V1 is dissipating power.

## Slide 50: Example 3
If voltage drops are given instead of currents, you need to apply Ohm’s Law to determine the current flowing through each of the resistors before you can find the current flowing out of the voltage supply.

## Slide 51: Example 3 (con’t)
For power dissipating components such as resistors, passive sign convention means that current flows into the resistor at the terminal has the + sign on the voltage drop and leaves out the terminal that has the – sign.

## Slide 52: Example 3 (con’t)

## Slide 53: Example 3 (con’t)
I1 is leaving the node.
I2 is entering the node.
I3 is entering the node.
I is entering the node.

## Slide 54: Example 4
Find the voltage across R1. Note that the polarity of the voltage has been assigned in the circuit schematic.
  First, define a loop that include R1.

## Slide 55: Example 4 (con’t)
There are three possible loops in this circuit – only two include R1.
  Either loop may be used to determine VR1.

## Slide 56: Example 4 (con’t)
If the outer loop is used:
  Follow the loop clockwise.

## Slide 57: Example 4 (con’t)
    Follow the loop in a clockwise direction.
    The 5V drop across V1 is a voltage rise.
    VR1 should be treated as a voltage rise.
    The loop enters on the positive side of the CURRENT source and exits out the negative side. This is a voltage drop as the voltage becomes less positive as you move through the component.

## Slide 58: Example 4 (con’t)
By convention, voltage drops are added and voltage rises are subtracted in KVL.

## Slide 59: Example 4 (con’t)
Suppose you chose the green loop instead.
  Since R2 is in parallel with I1, the voltage drop across R2 is also 3V.

## Slide 60: Example 4 (con’t)
    The 5V drop across V1 is a voltage rise.
    VR1 should be treated as a voltage rise.
    The loop enters R2 on the positive side and exits out the negative side. This is a voltage drop as the voltage becomes less positive as you move through the component.

## Slide 61: Example 4 (con’t)
As should happen, the answer is the same.

## Slide 62: Example 5
Find the voltage across R2 and the current flowing through it.
  First, draw a loop that includes R2.

## Slide 63: Example 5 (con’t)
There are two loops that include R2.
  The one on the left can be used to solve for VR2 immediately.

## Slide 64: Example 5 (con’t)
Following the loop in a clockwise direction.
  The 11.5V drop associated with V1 is a voltage rise.
  The 2.4V associated with R1 is a voltage drop.
  VR2 is treated as a voltage drop.

## Slide 65: Example 5 (con’t)

## Slide 66: Example 5 (con’t)
If you used the right-hand loop, the voltage drop across R3 must be calculated using Ohm’s Law.

## Slide 67: Example 5 (con’t)
  Since R3 is a resistor, passive convention means that the positive sign of the voltage drop will be assigned to the end of R3 where current enters the resistor.
  As I1 is in series with R3, the direction of current through R3 is determined by the direction of current flowing out of the current source.
  Because I1 and R3 are in series, the magnitude of the current flowing out of I1 must be equal to the magnitude of the current flowing out of R3.

## Slide 68: Example 5 (con’t)
Use Ohm’s Law to find VR3.

## Slide 69: Example 5 (con’t)
Moving clockwise around the loop:
  VR3 is a voltage drop.
  The voltage associated with I1 is a voltage drop.
  VR2 is a voltage rise.

## Slide 70: Example 5 (con’t)
Again, the same answer is found.

## Slide 71: Example 5 (con’t)
  Once the voltage across R2 is known, Ohm’s Law is applied to determine the current.
  The direction of positive current flow, based upon passive sign convention is shown in red.
IR2

## Slide 72: Example 5 (con’t)
IR2