## Slide 1: Additional Slides from Computer Networks by Tanenbaum and Wetheral

## Slide 2: Flooding (Taşkın)
Every incoming packet is sent out on every outgoing link except the one it arrived on
It generates vast number of duplicate packets
A hop counter is kept at the header of each packet which is decremented at each hop, with the packet being discarded when the counter reaches to zero
Keeping track of floooding packet could be an alternative technique to avoid sending them out second time
Selective flooding could be another alternative solution
It is very robust
It finds the shortest path

## Slide 3: Distance Vector Routing
(a) A network. (b) Input from A, I, H, K, and the new routing table for J.

## Slide 4: The Count-to-Infinity Problem
The count-to-infinity problem
The core of the problem is that when X tells Y that it has a path somewhere, Y has no way of knowing whether it itself is on the path.

## Slide 5: Link State Routing
Discover neighbors, learn network addresses.
Set distance/cost metric to each neighbor.
Construct packet telling all learned.
Send packet to, receive packets from other routers.
Compute shortest path to every other router.

## Slide 6: Building Link State Packets
(a) A network. (b) The link state packets for this network.

## Slide 7: Possible problems
Sequence numbers wrap around
If a router crashes, it will start with seq no 0!
If a sequence number gets corrupted
Solution: Age field which is decremented once per second while being kept in a router. If it gets zero, the packet will be discarded.
+ Some refinements: holding area and ACK

## Slide 8: Distributing the Link State Packets
The packet buffer for router B in previous slide